## Slide 1: NAVIGATING THE ROCKY ENVIRONMENTAL TERRAIN
Eastern Lenders Association
2023 Conference
March 13, 2023

## Slide 2: NAVIGATING THE ROCKY ENVIRONMENTAL TERRAIN PANEL
Moderator: Susan Monaco – Managing Director/Chief FHA Underwriter - Dwight Capital LLC
Panelists:
  Jacob Levine – Program Environmental Clearance Officer - HUD
  Frederick Shaw – Technical Specialist Branch Chief, NE Region – HUD
  Therese Fretwell – Regional Environmental Officer Region 2 – HUD
  Keith Bayer – Managing Director of Environmental Services, Dominion Due Diligence Group

## Slide 3: Our Topics Today:
Climate Change – examples, what does HUD want?
Pipelines
Wetlands
Fall Hazards
Updates: Adoption of New ASTM Standards (2/14/2024), renewal of Authorization Memo (Section 106), Noise
Questions?

## Slide 4: UPDATES

## Slide 5: New ASTM Standard
  ASTM E1527-21 - Standard Practice for Environmental Site Assessments: Phase I ESA Process was released on December 21, 2021.
  The MAP Guide requires the use of the most recent edition of industry standards to comply with environmental laws and regulations.
  The EPA deemed the new standard compliant with All Appropriate Inquiry (AAI) rule effective February 13, 2023.

## Slide 6: New ASTM Standard
  EPA will still recognize Phase I ESAs conducted in compliance with ASTM E1527-13 as compliant with the AAI Rule until one year after the effective date of February 13, 2023.
  HUD will in turn require the adoption of ASTM E1527-21 for all applications submitted effective February 14, 2024

## Slide 7: New ASTM Standard Updates
    Revisions to REC, HREC, and CREC definitions (though doesn’t adjust concepts) and all RECs, CRECs, and significant database must be included in the Conclusions section
    More explicit requirements to review historical research
    Revisions to site reconnaissance regarding specific items present AND not present
    Requirements for site plan and site photographs to be provided
    Specific notation of significant data gaps in the Findings section
    Requires opinions on additional investigations (though recommendations still not required)
    Emerging contaminants (e.g., per- and polyfluoroalkyl substances, or PFAS) included in non-scope considerations
See the AAI and ASTM E1527-21 Comparison posted by the EPA - https://www.regulations.gov/document/EPA-HQ-OLEM-2021-0946-0002

## Slide 8: Section 106 Authorization Memo
Formerly Known As the Delegation Memo
Extended Until December 2027
No major changes, but clarifies key points about tribal consultation and HUD’s responsibilities
Make sure to attach the new memo to SHPO consultation letters

## Slide 9: Noise Guidebook Update
Updated Noise Guidebook is still going through internal HUD review
LDAY is available for use on outdoor amenities that are closed at night, requires special approval
Housing is working on a new Fact Sheet that will cover LDAY and other key concepts from the Noise Guidebook

## Slide 10: Climate Change

## Slide 11: Climate Change
As outlined in the Administrative Memorandum “Guidance on Considering Climate Change in Environmental Assessment Factors for Multifamily Projects” signed by Willie Fobbs, after December 1, 2022, EA level applications must discuss reasonably foreseeable climate impacts over the life of the mortgage and address mitigation measures that would be prudent to implement at the construction stage.

## Slide 12: Climate EA Factor Fact Sheet
Report preferred at Pre-App, but mitigation measures may require updates at Firm application
List recent additional data sources, including the White House climate mapping tool for resilience and adaptation (CMRA), and the U.S. Global Change Research Program
Addressing National Risk Index categories that are not climate influenced (volcanic activity, earthquakes)

## Slide 13: Climate EA Factor Fact Sheet
How to analyze risks when robust data and projections aren’t available
  Infer from broader regional trends and projections
  Degree of confidence in risk level may affect mitigation decisions
Documenting analysis in HEROS
  Risk analysis, mitigation discussion, and overall determination in the Impact Evaluation column
  Only enter text in the Mitigation column if the project will include mitigation measures as a result of the climate risk analysis (don’t enter ‘N/A’ or ‘not required’)

## Slide 14: Climate Change
Extreme temperature, cold wave, and severe winter weather considerations: (EA Factors)
  Green Building certification being sought, if applicable
  Building envelope design features (windows, doors, and insulation) that work to mitigate both cold weather concerns, also considering additional air and gap sealing efforts to limit exterior air infiltration.
  Window treatments to provide additional cold weather shielding to resident living spaces
  Specific local building code requirements that specifically work to address cold weather concerns (e.g., roof snow loads, building envelope requirements, utility infrastructure requirements, etc.)
  Local early emergency notification systems, and any other planned notification and educational resources for future residents
  Consideration for making the community center a resiliency hub in the event of a severe weather event.

## Slide 15: Climate Change
Flooding considerations:
  Review all effective, preliminary, and pending FEMA floodplain maps to determine site-specific conditions. HUD’s regulations in 24 CFR Part 55 and compliance with EO 11988 will drive the baseline measures.
  For properties outside of the 100 and 500-year floodplain, additional considerations are less likely to be warranted, but are still possible.
  For properties within the 500-year floodplain, additional flood proofing measures should be considered.
  Sewer backup flooding can be a big issue!
  Local early emergency notification systems, and any other planned notification and educational resources for future residents
  Consideration for making the community center a resiliency hub in the event of a severe flooding event.

## Slide 16: Climate Change
Tornado and hurricane considerations:
  Specific local building code wind load requirements, with considerations for building envelope proposed construction features.
  Local early emergency notification systems, and any other planned notification and educational resources for future residents
  Consideration for making the community center a resiliency hub in the event of a severe weather event.
  For hurricanes, additional flood proofing considerations may be warranted.
  Coordinate with emergency management at the municipal or county level. Is an Evacuation plan needed?

## Slide 17: Climate Change
Lightning considerations:
  Specific local building code wind load requirements, with considerations for building envelope proposed construction features.
  Local early tornado emergency notification systems, and any other planned notification and educational resources for future residents
  Consideration for making the community center a resiliency hub in the event of a tornado event.
General considerations:
  Review the applicable state and local hazard mitigation plans and consider similar design features being implementing into local infrastructure.

## Slide 18: Climate Change
Additional Resources:
  HUD Exchange EA Factors eGuide - https://www.hudexchange.info/programs/environmental-review/environmental-assessment/guide/climate-and-energy/
  HUD Exchange Climate Change EA Factor Fact Sheet - https://www.hudexchange.info/programs/environmental-review/environmental-assessment/guide/climate-and-energy/
  FEMA National Risk Index - https://hazards.fema.gov/nri/map
  FEMA Hazard Mitigation Plan Status - https://fema.maps.arcgis.com/apps/webappviewer/index.html?id=ec2fb023df744cf480da89539338c386
  FEMA Hazard Mitigation Planning - https://www.fema.gov/emergency-managers/risk-management/hazard-mitigation-planning

## Slide 19: Pressurized Pipelines

## Slide 20: Pressurized Pipeline Incident Example
In August 2019, a 30” natural gas pipeline owned and operated by Enbridge, Inc. exploded, severely impacting a ¼ mile area and killing one person:

## Slide 21: Pressurized Pipeline Incident Example
The National Transportation Safety Board (NTSB) conducted an investigation on the incident and determined the following:
Pre-existing hard spots (a manufacturing defect), degraded coating, and ineffective cathodic protection applied following a 2014 gas flow reversal project resulted in hydrogen-induced cracking at the outer surface of the pipeline and its subsequent failure.
NTSB determined that the use of the Pipeline Impact Radius (PIR) equation did not include the full area at risk.
  Note that HUD uses a more
  restrictive PIR equation

## Slide 22
9.6.19.A: For ALL PROJECTS, the easement of a pressurized pipeline (pipelines exceeding 200 psi maximum operating pressure) must be at least 10 feet away from structures, ancillary facilities, common areas, parking areas or like related improvements. This does not apply to distribution lines supplying only the facility itself.
Pressurized Pipelines
9.6.19.B: For NC projects and SR projects where residential density is increased, must also assess the Potential Impact Radius (PIR) of above-ground and below-ground pressurized pipelines within a mile of the property. This includes onsite or immediately adjacent pipelines.
*Reminders*

## Slide 23
Pressurized Pipelines
Please also note that HUD released a Fact Sheet to clarify and expand on the pressurized pipeline requirements outlined in the MAP Guide.
https://www.hudexchange.info/programs/environmental-review/housing/fact-sheets/#map-guide-on-acceptable-separation-distance-and-pipelines
The Fact Sheet includes eleven (11) points of clarity and additional guidance with the two (2) subcategories listed below.

## Slide 24: Pressurized Pipelines – What Will HUD Accept?
For buildings and structures
  Underground pipeline depth of 3+ feet
For outdoor ancillary facilities or common areas
  Underground pipeline depth of 6+ feet
For both buildings and structures AND outdoor ancillary facilities or common areas
  Can’t be within 10 feet of the easement of pressurized pipeline (9.6.19.A)
  Soil overburden between the project and pipeline has a high bearing capacity
  Pipeline segment has passed its most recent inspection report with no unresolved violations.

## Slide 25: Pressurized Pipelines – What Will HUD Accept?
If the buildings/structures and outdoor ancillary facilities and common areas conditions do not apply:
  The engineering report must discuss whether other existing barriers such as roads built to Federal Department of Transportation (DoT) standards, topography, walls or buildings provide mitigation or whether the project must add additional mitigation to protect residents from thermal radiation.

## Slide 26
Pressurized Pipelines
HUD further defined the requirements of the engineering report within their Fact Sheet:
Must be conducted and stamped by a licensed P.E. and should include the following:
  Distance from pipeline to project site
  The pipeline’s most recent inspection report
  Conditions of the specific pipeline segment such as corrosion, damage, defects, deferred maintenance and historical incidents such as leaks or releases
  Pipeline depth or pipeline aboveground exposure
  Type of soil in soil column from pipeline to project from Geotech survey or U.S. Department of Agriculture (USDA) soil survey map

## Slide 27: Pressurized Pipeline Example

## Slide 28: Pressurized Pipeline Mitigation Example
Mitigation example:
  HUD MAP 221(d)(4) new construction
  The licensed P.E. recommended that a 6’ tall, 8” thick, 4,000 psi concrete wall with continuous footing with 3,000 psi concrete be installed along the denoted 625 linear foot area of concern.

## Slide 29: Pressurized Pipelines – The Good News!
HUD will accept PE recommendations as long as it meets HUD requirements and references HUD’s prescribed thermal heat flux threshold and blast overpressure threshold.
HUD has added a formula for estimating pressure to the pipeline fact sheet. This can be used as a last resort if the operator will not provide the pressure.​
Nelson’s position has been posted.

## Slide 30: Wetlands

## Slide 31: Wetlands
E.O. 11990 – Protection of Wetlands: Issued May 24, 1977 by President Carter.
Purpose is “to avoid to the extent possible the long and short term adverse impacts associated with the destruction or modification of wetlands and to avoid direct or indirect support of new construction in wetlands wherever there is a practicable alternative[.]”

## Slide 32: Wetlands
E.O. 11990 vs. 404 Clean Water Act
E.O. 11990 Sec. 7(c): “Those areas that are inundated by surface or ground water with a frequency sufficient to support and under normal circumstances does or would support a prevalence of vegetative or aquatic life that requires saturated or seasonally saturated soil conditions for growth and reproduction. Wetlands generally include swamps, marshes, bogs, and similar areas such as sloughs, potholes, wet meadows, river overflows, mud flats, and natural ponds.“ EO is more explicit due to a greater number of examples.​
Section 404, 33 CFR 328.3(b): “The term wetlands means those areas that are inundated or saturated by surface or ground water at a frequency and duration sufficient to support, and that under normal circumstances do support, a prevalence of vegetation typically adapted for life in saturated soil conditions. Wetlands generally include swamps, marshes, bogs, and similar areas.”
​
Similar wetlands definitions but differ in application:​

## Slide 33: Wetlands E.O. 11990 vs. 404 Clean Water Act (“CWA”) Differences
E.O. 11990:
Condition attached to federal spending; Spending power is broad in regards to conditions (see South Dakota v. Dole and NFIP)
Only limited by E.O. language, agency interpretation, and federal statutes
Applies to any wetland even if isolated, not navigable, or without a “requisite nexus” to such waters
404 Permits:
Regulatory in nature
Limited by CWA language “navigable waters” and those waters with a “requisite nexus” to such waters a.k.a “Waters of the United States” in CWA-speak
Requisite nexus requires an evaluation of hydrologic, ecologic, and geographic factors
The commerce clause is also a limitation

## Slide 34: Wetlands E.O. 11990 vs. 404 CWA Differences (continued)
404 jurisdiction can be somewhat ambiguous but basically limited to:
Traditional navigable waters
Tributaries of the above that are relatively permanent (flow year round or continuous flow seasonally, typically three months)
Adjacent waters
Isolated water with “Commerce Clause” connection
Excludes prior converted cropland
Note: EO 11990 is only limited by its language/agency interpretation or specific statutory provisions

## Slide 35: Wetlands
Sources for Wetlands Identification:
Army Corp of Engineers (ACE): https://www.nwp.usace.army.mil/Missions/Regulatory/Jurisdiction/#:~:text=Recognizing%20wetlands&text=Those%20areas%20that%20are%20inundated,life%20in%20saturated%20soil%20conditions.
Fish and Wildlife Services Classification Manual: https://www.fws.gov/wetlands/documents/classification-of-wetlands-and-deepwater-habitats-of-the-united-states.pdf

## Slide 36: Wetlands
NWI Maps as initial screening tool
Delineation survey vs Overlay
USFWS contact (when) (1st contact) vs Wetlands Specialist
When is an 8-step needed? Direct or indirect impacts.
Incidental Exceptions
Restrictive covenants and closing procedures.

## Slide 37: Restrictive Covenants and Other Assurances
For on-site wetlands not impacted by the project, HUD requires assurance that no future wetlands impacts will occur without HUD approval.
This often entails a restrictive covenant
Essential to reach early agreement on covenant language to avoid closing delays

## Slide 38: Fall Hazards

## Slide 39: Fall Hazards Fact Sheet
HUD released a Fall Hazards Fact Sheet - https://www.hudexchange.info/programs/environmental-review/housing/fact-sheets/#fall-hazards
Expanded definition of ‘ancillary facilities’ and ‘common areas’
Provides voltage ratings that define easement and fall hazard analysis requirements
Defines why buildings/ancillary facilities are prohibited within easements
Provides additional resources and links to online datasets

## Slide 40: Fall Hazards – Ancillary Facilities and Common Areas
Ancillary facilities include onsite areas that are not residential buildings, but are there to support or complement residential buildings and are used by people:
  Private balconies, front or back yards, divided green space or patios, carports, garages, sheds and pergolas or buildings like gyms, pool houses, etc.
Common areas are areas where people would likely congregate:
  Playgrounds and outdoor recreation areas. Parking lots included within the site boundaries of, and designed to serve the residents of, a HUD-insured residential or mixed-use development are covered under this definition.

## Slide 41: Fall Hazards – Voltage Ratings
69 kV or higher – transmission lines (high-voltage)
  Requires compliance with both easement and fall hazard analysis requirements
Between 50 and 69 kV:
  Requires compliance with fall hazard analysis requirements, but not easement requirements
50 kV or lower – local service lines:
  Does not require compliance with either easement or fall hazard analysis requirements
  *Note that HUD staff can evaluate whether any powerlines crossing a project site may pose a risk to residents or occupants.

## Slide 42: Fall Hazards – Voltage Ratings
Voltage Ratings

## Slide 43: Fall Hazards – Easement Restrictions
No buildings, ancillary facilities, structures or common areas allowed within any easement of transmission lines carrying 69 kV or higher.
  The easements of transmission lines create additional nuisances and hazards that merit the restriction on buildings and ancillary facilities altogether. These nuisances and hazards include:
    Electromagnetic fields
    Noise
    Sparks from electric arcs
    Access for utility maintenance activities

## Slide 44: Fall Hazards – Additional Resources
Contact the utility provider directly
Maps of some powerlines are publicly available through the US Energy Information Administration and Department of Homeland Security

## Slide 45
QUESTIONS? THANK YOU!